PRODUCTS

MANUFACTURERS

Provide Megapixel IP camera with streaming video technology by one of the following manufacturers:

ACTi

Megapixel Camera

Provide ACTi Model B64 Megapixel camera with features and characteristics as follows:

Imaging

Image Sensor: Progressive Scan CMOS

Sensor Size: 1/3 inch

Minimum Scene Illumination

Color: 0.1 Lux at F1.2 (2400 ºK, 30 IRE).

Black and White: 0 Lux (IR LED on).

IR Illuminators

IR Sensitivity Range: 700 – 1100 nm

Adaptive IR LED x 10 (850 nm)

IR Working Distance: 20 m (0 Lux, 30 IRE, Max exposure gain)

Lens

Focal Length: Zoom, f3 ~ 9 mm

Aperture: F1.2 ~ F2.1

Zoom Ratio: 3x optical

Zoom Speed : 1 sec (1x to 3x)

Iris: DC Iris

Focus: Auto Focus

Lens Mount Type: Board Mount

Horizontal Viewing Angle: 90.6°- 31.8°

Viewing Angle Adjustment: Pan: 0° - 350°°; Tilt: 5° - 170°; Rotate:0°-350°

Day/ Night

Day/Night switching : ISP based switch, configurable

Mechanical IR Cut Filter: Yes

Electronic Shutter:

Manual Mode : 1/5 – 1/2,000 sec

Auto Mode : 1/5 – 1/10,000 sec

Functions

Superior Low Light Sensitivity (SLLS) : Automatic

Basic WDR (83.5 dB)

White Balance: Auto/ hold /manual.

Brightness

Contrast

Automatic Sharpness

Automatic Gain Control

Digital Noise Reduction

Flickerless

Image Orientation: Image Flip / Image Mirror

Text Overlay: User defined text on video

Provide at least 32 Zoom preset points

On-Screen Graphics: User defined image layer on video

Alarm:

14.1 Alarm Trigger:

Video motion detection: 3 motion regions

            - External device through digital input

14.2   Alarm Response:

a. Notify control center

b. Go to Zoom preset point or preset tour

c. Change camera settings

d. Command other devices

e. E-mail notification with snapshots

f. Save video or snapshot to local storage

g. Upload video, snapshot to FTP server

h. Activate external device through digital output

Compression: H.264 (High Profile)/ MJPEG.

Picture Resolution:

1280 x 960

1280 x 720

640 x 480

320 x 240

Maximum Image Frame Rate:

30 fps at 1280 x 960

60 fps at 1280 x 720

30 fps at 640 x 480

15 fps at 320 x 240

Bit Rate: 28k – 6Mbps per stream; Support Constant and Variable Bit Rate Mode.

Multi-Streaming: Simultaneous dual streams based on two configurations.

Audio

Audio: two-way

Compression: PCM 8 kHz, 16 bit encoding, mono; G.711 aLaw/uLaw

Audio Input: 1, Terminal block

Audio Output: 1, Terminal block

Digital Inputs/ Outputs:

Digital Inputs:  2 inputs, terminal block.

Digital Output: 2 outputs, terminal block.

Local Storage:

MicroSDHC/MicroSDXC memory card slot(card not included)

External Buttons:

Factory default Button : 1 ,reset to factory default setting

Networking

Network Port: 1, Ethernet (10/100Base-T) via RJ-45 connector.

Protocol: TCP, UDP, HTTP, HTTPS, DHCP, PPPoE, RTP, RTSP, IPv4, IPv6, DNS, DDNS, NTP, ICMP, ARP, IGMP, SMTP, FTP, UPnP, SNMP, Bonjour, ONVIF  Compliant.

Security: IP address filtering; HTTPS encryption; Password protected user levels; Anonymous login; IEEE 802.1X network access control.

Integration

Unified Solution : Fully compatible with ACTi software

ISV Integration: Software Development Kit(SDK) available ; ONVIF Compliant

Firmware Access Browser: Microsoft Internet Explorer 8.0 or newer (full functionality); Other browsers with QuickTime installed (partial functionality)

Power Source / Consumption

DC Power : 12 VDC / 4.8W (adapter not included)

PoE Class 3 (IEEE802.3af) / 5.8W

Physical Characteristics:

Dimensions (Ø x H): 146 mm x 107 mm (5.7” x 4.2”)

Weight: 719g (1.58 lb)

Environmental Casing

Vandal Resistant (IK09)

Transparent Dome Cover

Mount Type

Surface, Pendant, Wall, Corner, Pole, Flush, Gang Box

Operating Temperature

Starting Temperature: -10ºC - 50ºC (14ºF - 122ºF)

Operating Temperature: -10ºC - 50ºC (14ºF - 122ºF)

Operating Relative Humidity: 10% ~ 85% RH

Approvals:

Camera: CE (EN 55022 Class B, EN 55024), FCC (Part15 Subpart B Class B), IK09

Warranty:

3 years

END OF SECTION