PRODUCTS

MANUFACTURERS

Provide Megapixel IP camera with streaming video technology by one of the following manufacturers:

ACTi

Megapixel Camera

Provide ACTi Model B97 Megapixel camera with features and characteristics as follows:

Imaging

Image Sensor: Progressive Scan CMOS

Sensor Size: 1/3 inch

Minimum Scene Illumination

Color: 0.1 Lux at F1.8 (30 IRE, 2400 ºK)

Black and White: 0.05 Lux at F1.8 (30 IRE, 2400 ºK)

IR Illuminators

IR Sensitivity Range: 700 – 1100 nm

Lens

Focal Length: Zoom, f4.9~49 mm

Aperture: F1.8~F3.0

Zoom Ratio: 10x optical

Zoom Speed : Max 2sec (1x to 10x)

Iris: DC Iris

Focus: Auto Focus

Lens Mount Type: Board Mount

Horizontal Viewing Angle: 49.56º - 5.62º

PTZ

Manual Panning Speed:  5°~ 50°/s

Manual Tilting Speed: 5°~  50°/s

Preset Panning Speed: 5° ~ 70°/s

Preset Tilting Speed: 5° ~ 70°/s

Panning Range: -175° ~ 175° (without auto-flip)

Tilting Range: 0~180° (with E-flip)

Control: Remote manual control; 256 preset points; 10 preset tours; Auto scan

Preset Panning Accuracy: 1.5°

Preset Tilting Accuracy: 1.5°

Absolute Position : Yes

Protocol: ACTi URL command, Sony VISCA, Pelco-D, Pelco-P

Day/ Night

Day/Night switching : ISP based switch, configurable

Mechanical IR Cut Filter: Yes

Electronic Shutter:

Manual Mode : 1/5 –1/2,000 sec

Auto Mode : 1/5 – 1/10,000 sec

Functions

Superior WDR (107 dB)

White Balance: Auto/ hold /manual.

Brightness

Contrast

Automatic Sharpness

Automatic Gain Control

Digital Noise Reduction

Flickerless

Image Orientation: Image Flip / Image Mirror

Text Overlay: User defined text on video

On-Screen Graphics: User defined image layer on video

Alarm:

12.1 Alarm Trigger:

Video motion detection: 3 motion regions

            - External device through digital input

12.2   Alarm Response:

a. Notify control center

b. Go to PTZ preset point or preset tour

c. Change camera settings

d. Command other devices

e. E-mail notification with snapshots

f. Save video or snapshot to local storage

g. Upload video, snapshot to FTP server

h. Activate external device through digital output

Compression: H.264 (High Profile)/ MJPEG.

Picture Resolution:

2048 x 1536

1920 x 1080 (Full HD 1080p)

1280 x 720 (HD 720p)

640 x 480 (VGA)

320 x 240 (QVGA)

Maximum Image Frame Rate:

15 fps at 2048 x 1536

15 fps at 1920 x 1080 (Full HD 1080p)

30 fps at 1280 x 720 (HD 720p)

30 fps at 640 x 480 (VGA)

15 fps at 320 x 240 (QVGA)

Bit Rate: 28k – 6Mbps per stream; Support Constant and Variable Bit Rate Mode.

Multi-Streaming: Simultaneous dual streams based on two configurations.

Audio

Audio: two-way

Compression: PCM 8 kHz, 16 bit encoding, mono; G.711 aLaw/uLaw

Audio Input: 1, Terminal block

Audio Output: 1, Terminal block

Interface:

External Button: Reset button for factory default setting

Local Storage: MicroSDHC/MicroSDXC memory card slot(card not included)

Digital Input:  1, Terminal block.

Digital Output: 1, Terminal block

Networking

Network Port: 1, Ethernet (10/100Base-T) via RJ-45 connector.

Protocol: TCP, UDP, HTTP, HTTPS, DHCP, PPPoE, RTP, RTSP, IPv4, IPv6, DNS, DDNS, NTP, ICMP, ARP, IGMP, SMTP, FTP, UPnP, SNMP, Bonjour, ONVIF Compliant.

Security: IP address filtering; HTTPS encryption; Password protected user levels; Anonymous login; IEEE 802.1X network access control.

Integration

Unified Solution : Fully compatible with ACTi software

ISV Integration: Software Development Kit(SDK) available ; ONVIF Compliant

Firmware Access Browser: Microsoft Internet Explorer 8.0 or newer (full functionality); Other browsers with QuickTime installed (partial functionality)

Power Source / Consumption

DC Power : 12 VDC / 10.36W

PoE Class 3 (IEEE802.3af) / 12.95W

Physical Characteristics:

Dimensions (Ø x H): 152 mm x 118 mm (6” x 4.7”)

Weight: 1263 g (2.784 lb)

Environmental Casing

Weatherproof (IP66 rated)

Vandal Proof (IK10 rated)

Transparent Dome Cover

Mount Type:

Surface, Pendant, Wall, Corner, Pole, Flush, Gang Box

Operating Temperature

Starting Temperature: -20ºC - 50ºC (-4ºF - 122ºF) with 30 mins

Operating Temperature:-20ºC - 50ºC (-4ºF - 122ºF)

Operating Relative Humidity: 10% ~ 85% RH

Approvals:

CE (EN 55022 Class B, EN 55024), FCC (Part15 Subpart B Class B), IP66,

NEMA 4X, IK10

Warranty:

Camera:

3 years (in occasional motion)

3 months (in continuous motion)

Adapter: 1 year

END OF SECTION