PRODUCTS

MANUFACTURERS

Provide Megapixel IP camera with streaming video technology by one of the following manufacturers:

ACTi

Megapixel Camera

Provide ACTi Model D12 Megapixel cube camera with features and characteristics as follows:

Imaging

Image Sensor: Progressive Scan CMOS

Sensor Size: 1/3.2 inch

Minimum Scene Illumination

Color: 0.1 Lux at F2.0 (2400 ºK, 30 IRE).

Lens

Focal Length: Fixed focal, f3.6 mm

Aperture: F2.0

Iris: Fixed Iris

Focus: Fixed focus

Lens Mount: Board Mount

Horizontal Viewing Angle: 70.8º

Electronic Shutter:

Manual Mode : 1/5 – 1/2000 sec

Auto Mode : 1/5 – 1/10,000 sec

Functions

White Balance: Auto/ hold /manual.

Brightness

Contrast

Automatic Sharpness

Automatic Gain Control

Digital Noise Reduction

Flickerless

Image Orientation: Image Flip / Image Mirror

Privacy Masks: 4 configurable regions

Text Overlay: User defined text on video

On-Screen Graphics: User defined image layer on video

Alarm:

12.1 Alarm Trigger:

Video motion detection: 3 motion regions

12.2   Alarm Response:

a. Notify control center

b. Change camera settings

c. Command other devices

d. E-mail notification with snapshots

e. Upload video, snapshot to FTP server

Compression: H.264 (High Profile)/ MJPEG.

Picture Resolution:

2048 x 1536

1920 x 1080 (Full HD 1080p)

1280 x 720 (HD 720p)

640 x 480 (VGA)

Maximum Image Frame Rate:

15 fps at 2048 x 1536

30 fps at 1920 x 1080 (Full HD 1080p)

30 fps at 1280 x 720 (HD 720p)

30 fps at 640 x 480 (VGA)

Bit Rate: 28k – 6Mbps per stream; Support Constant and Variable Bit Rate Mode.

Multi-Streaming: Simultaneous dual streams based on two configurations.

Interface:

External Buttons: Reset button for factory default setting

Networking

Network Port: 1, Ethernet (10/100Base-T) via RJ-45 connector.

Protocol: TCP, UDP, HTTP, HTTPS, DHCP, PPPoE, RTP, RTSP, IPv4, IPv6, DNS, DDNS, NTP, ICMP, ARP, IGMP, SMTP, FTP, UPnP, SNMP, Bonjour, ONVIF 2.2 Compliant.

Security: IP address filtering; HTTPS encryption; Password protected user levels; Anonymous login; IEEE 802.1X network access control.

Integration

Unified Solution : Fully compatible with ACTi software

ISV Integration: Software Development Kit(SDK) available ; ONVIF 2.2 compliant

Firmware Access Browser: Microsoft Internet Explorer 8.0 or newer (full functionality); Other browsers with VLC installed (partial functionality)

Mount Type:

Wall, Ceiling

Power Source / Consumption

PoE Class 2 (IEEE802.3af) / 3.7 W

Physical Characteristics:

Dimensions (W x H x D): 66.50 mm x 103.95 mm x 38.75 mm (2.62” x 4.09” x 1.53”)

Weight: 140g (0.31 lb)

Operating Temperature

-10ºC - 45ºC (14ºF - 113ºF)

Operating Relative Humidity: 10% ~ 85% RH

Approvals:

CE (EN 55022 Class B, EN 55024), FCC (Part15 Subpart B Class B)

Warranty:

2 years

END OF SECTION