PRODUCTS

MANUFACTURERS

Provide Megapixel IP camera with streaming video technology by one of the following manufacturers:

ACTi

Megapixel Camera

Provide ACTi Model I93 Megapixel camera with features and characteristics as follows:

Imaging

Image Sensor: Progressive Scan CMOS

Sensor Size: 1/2.8 inch

Minimum Scene Illumination

Color: 0.1 Lux at F1.6 (2400 ºK, 30 IRE).

Black and White: 0.05 Lux at F1.6 (2400 ºK, 30 IRE).

IR Illuminators

IR Sensitivity Range: 700 – 1100 nm

Lens

Focal Length: Zoom, f4.3~129 mm

Aperture: F1.6~F5.0

Zoom Ratio: 30x optical , 16x digital

Zoom Speed : 2.87 sec (1x to 30x)

Iris: DC Iris

Focus: Auto Focus

Lens Mount Type: Board Mount

Horizontal Viewing Angle: 66.4° ~ 2.68°

PTZ

Manual Panning Speed:  0.5°~ 90°/s

Manual Tilting Speed: 0.5°~  90°/s

Preset Panning Speed: 0.5° ~ 450°/s

Preset Tilting Speed: 0.5° ~ 450°/s

Panning Range: 0° ~ 360° (with Auto-flip)

Tilting Range: 0° ~ 180°

Control: Remote manual control; 256 preset points; 10 preset tours; Auto scan

Preset Panning Accuracy: 0.265°

Preset Tilting Accuracy: 0.265°

Absolute Position : Yes

Protocol: ACTi URL command, Sony VISCA, Pelco-D, Pelco-P

Day/ Night

Day/Night switching : ISP based switch, configurable

Mechanical IR Cut Filter: Yes

Electronic Shutter:

Manual Mode : 1/5 –1/2,000 sec

Auto Mode : 1/5 – 1/10,000 sec

Functions

Superior Low Light Sensitivity (SLLS) : Automatic

Extreme WDR (107 dB)

White Balance: Auto/ hold /manual.

Brightness

Contrast

Automatic Sharpness

Automatic Gain Control

2D+3D Digital Noise Reduction

Defogging

Advanced Image Stabilizer

Flickerless

Image Orientation: Image Flip / Image Mirror

Privacy Masks: 4 configurable regions

Text Overlay: User defined text on video

On-Screen Graphics: User defined image layer on video

Alarm:

16.1 Alarm Trigger:

Video motion detection: 3 motion regions

            - External device through digital input

16.2   Alarm Response:

a. Notify control center

b. Go to PTZ preset point or preset tour

c. Change camera settings

d. Command other devices

e. E-mail notification with snapshots

f. Save video or snapshot to local storage

g. Upload video, snapshot to FTP server

h. Activate external device through digital output

Compression: H.264 (High Profile)/ MJPEG.

Video Resolution:

1280 x 720 (HD 720p)

640 x 480 (VGA)

320 x 240 (QVGA)

Maximum Image Frame Rate:

30 fps at 1280 x 720 (HD 720p)

30 fps at 640 x 480 (VGA)

15 fps at 320 x 240 (QVGA)

Bit Rate: 28k – 6Mbps per stream; Support Constant and Variable Bit Rate Mode.

Multi-Streaming: Simultaneous dual streams based on two configurations.

Audio

Audio: two-way

Compression: PCM 8 kHz, 16 bit encoding, mono; G.711 aLaw/uLaw

Audio Input: Cable with 3.5mm Phone Jack

Audio Output: Cable with 3.5mm Phone Jack

Interface:

External Button: System reboot button ; Reset button for factory default setting

Local Storage: MicroSDHC/MicroSDXC memory card slot(card not included)

Digital Inputs:  4, cable without connector

Digital Outputs: 2, cable without connector

Networking

Network Port: 1, Ethernet (10/100Base-T) via RJ-45 connector.

Protocol: TCP, UDP, HTTP, HTTPS, DHCP, PPPoE, RTP, RTSP, IPv4, IPv6, DNS, DDNS, NTP, ICMP, ARP, IGMP, SMTP, FTP, UPnP, SNMP, Bonjour, ONVIF Compliant.

Security: IP address filtering; HTTPS encryption; Password protected user levels; Anonymous login; IEEE 802.1X network access control.

Integration

Unified Solution : Fully compatible with ACTi software

ISV Integration: Software Development Kit(SDK) available ; ONVIF Compliant

Firmware Access Browser: Microsoft Internet Explorer 8.0 or newer (full functionality); Other browsers with QuickTime installed (partial functionality)

Power Source / Consumption

AC Power : 24 VAC / 31.5W (with heater and fan on)

PoE: High PoE (IEEE802.3af) / 25.44W (with heater and fan on)

Physical Characteristics:

Dimensions (Ø x H): 200 mm x 276 mm (7.9” x 10.9”)

Weight: 2500g (5.51 lb)

Environmental Casing

Weatherproof (IP66)

Vandal proof casing (IK10)

Bundled dome cover (IK09)

Optional dome cover (IK10)

Mount Type

Pendant, Wall, Corner, Pole

Operating Temperature

Starting Temperature: -40ºC - 50ºC (-40ºF - 122ºF) within 30 minutes

Operating Temperature: -40ºC - 50ºC (-40ºF - 122ºF)

Operating Relative Humidity: 10% ~ 85% RH

Approvals:

Camera: CE (EN 55022 Class B, EN 55024), FCC (Part15 Subpart B Class B), IP66, NEMA 4X, IK09

Warranty:

Camera:

3 years (in occasional motion)

1 year (in continuous motion)

Adapter: 1 year

END OF SECTION